## Slide 1: Nursing And USP<800>: What’s different from NIOSH and WA Law?
Seth Eisenberg RN OCN® BTMCN®

## Slide 2: Comparison: Gloves
NIOSH | Washington State | USP<800>
Double chemotherapy gloves (ASTM rated) for chemotherapy; consider for non-antineoplastic HDs. | Powder-free chemotherapy gloves when handling chemotherapy drugs or when there is potential contact with chemotherapy contaminated items or surfaces | Two pairs of chemotherapy gloves are required. Must meet American Society for Testing and Materials (ASTM) standard D6978 (or its successor).
For all activities associated with drug administration. | Two pairs of gloves when there is a “significant risk of breakage or contamination or permeation,” e.g., during compounding, extended handling periods, and cleaning up large HD spills | Required for administering antineoplastic HDs, including non-antineoplastics and for reproductive risk only HDs.

## Slide 3: Comparison: Gowns
NIOSH | Washington State | USP<800>
Disposable, with long sleeves, elastic or knit cuffs, and closed fronts. | Disposable, closed front, long sleeves, and elastic or knit cuffs made of polyethylene-coated polypropylene or other nonabsorbent, nonlinting protective material as determined by the PPE hazard assessment. | Disposable, with ability to resist chemotherapy; long sleeves, elastic or knit cuffs, closed front, and without seams or closures that could allow HD exposure.
Wear gowns for all activities associated with drug administration— opening the outer bag, assembling the delivery system, delivering the drug to the patient, and disposing of all equipment used for administration. | Wear gowns whenever there is a reasonable possibility of a hazardous drug splash or spill such as in compounding, preparing and administering. Remove and dispose of gowns at the end of hazardous drug handling activities, when leaving the hazardous drug handling area and as soon as possible when damaged or contaminated | Appropriate PPE must be worn when administering HDs. After use, PPE must be removed and disposed of in a waste container approved for trace-contaminated HD waste at the site of drug administration. Cloth laboratory coats, scrubs, and isolation gowns are prohibited. Must not be worn outside of HD handling areas.

## Slide 4: Comparison: Respiratory Protection
NIOSH | Washington State | USP<800>
Refers to general OSHA recommendations [29 CFR 1910.134] and CDC [42 CFR 84]. Does not specify type or use. | Use appropriate respiratory protection or equivalent respiratory protection during spill cleanup and whenever there is a significant risk of inhalation exposure to hazardous drug particulates | If risk of respiratory exposure when cleaning spills is “larger than what can be contained with a spill kit,” and if “a known or suspected airborne exposure to powders or vapors” occurs.
 | Use an appropriate chemical cartridge-type respirator for events such as large spills of volatile hazardous drugs, e.g., when an intravenous (IV) bag breaks or a line disconnects | Full-face chemical cartridge respirator or PAPR.

## Slide 5: Comparison: CSTDs
NIOSH | Washington State | USP<800>
Consider CSTDs to protect nursing personnel during drug administration. | Mentioned as example in hazard assessment. | Required for administration of antineoplastic HDs when dosage form allows.
 | Evaluate and implement appropriate engineering controls to eliminate or minimize employee exposure. Examples of engineering controls include, but are not limited to: CSTDs… | 

## Slide 6: Comparison: Education
NIOSH | Washington State | USP<800>
Regular training for all personnel handing HDs. | HD training to all employees with occupational exposure at the time of their initial job assignment and whenever a new HD or a new process related to handling an HD that the employees have not previously been trained is introduced into their work area. | Training required prior to handling HDs, and annually thereafter. All training and competency assessment must be documented.
 |  | Must include: Overview of entity's list of HDs and their risks; HD SOPs; proper use of PPE and devices; Spill management and response to exposure; Proper disposal of HDs and trace-contaminated materials