## Slide 1: Occupational Exposure to Lead
Cheryl Christian, MS CIH
Division of Occupational Safety & Health (DOSH)
Laboratory and Technical Services
Industrial Hygienist
September 14, 2015

## Slide 2
L&I has distinct roles with lead exposure:
Division of Occupational Safety and Health (DOSH)
  Federal OSHA audited state plan grant as the safety and health regulatory administration for State of Washington
  Regulatory compliance to ensure employers meet obligations to provide safe workplaces for workers
  Compliance, Consultation, Education services
Safety & Health Assessment and Research for Prevention (SHARP) Program
Administering the state Worker’s Compensation Fund
2
Notes: Purpose. RCW (49.17)
The legislature finds that personal injuries and illnesses arising out of conditions of employment impose a substantial burden upon employers and employees in terms of lost production, wage loss, medical expenses, and payment of benefits under the industrial insurance act. Therefore, in the public interest for the welfare of the people of the state of Washington and in order to assure, insofar as may reasonably be possible, safe and healthful working conditions for every man and woman working in the state of Washington, the legislature in the exercise of its police power, and in keeping with the mandates of Article II, section 35 of the state Constitution, declares its purpose by the provisions of this chapter to create, maintain, continue, and enhance the industrial safety and health program of the state, which program shall equal or exceed the standards prescribed by the Occupational Safety and Health Act of 1970 (Public Law 91-596, 84 Stat. 1590).
RCW 49.17.050
(2) Provide for the adoption of occupational health and safety standards which are at least as effective as those adopted or recognized by the United States secretary of labor under the authority of the Occupational Safety and Health Act of 1970 (Public Law 91-596; 84 Stat. 1590); (4) Provide for the promulgation of health and safety standards and the control of conditions in all workplaces concerning gases, vapors, dust, or other airborne particles, toxic materials, or harmful physical agents which shall set a standard which most adequately assures, to the extent feasible, on the basis of the best available evidence, that no employee will suffer material impairment of health or functional capacity even if such employee has regular exposure to the hazard dealt with by such standard for the period of his or her working life; any such standards shall require where appropriate the use of protective devices or equipment and for monitoring or measuring any such gases, vapors, dust, or other airborne particles, toxic materials, or harmful physical agents;
  Research program at L&I. Purpose is to prevent workplace injury and illness and to discover new emerging hazards and conditions in Washington workplaces. Not part of DOSH or Workers Compensation.
  Administers WA Adult Blood Lead Epidemiology and Surveillance program (ABLES) among many other programs
  Insurance Services for state workers compensation fund – lost time, medical expenses, disability

## Slide 3: DOSH
Washington state “State Plan” State
  “At least as effective as” OSHA rules and policies
Must have employer/employee relationship for jurisdiction
  Jurisdiction includes public employees
Two primary rules for worker lead exposure:
  General Industry WAC 296-62-07521
  Construction WAC 296-155-176
When evaluating for lead on the jobsite, other rules also commonly apply, such as:
  respiratory protection
  personal protective equipment
3
Notes: General industry – All occupational exposures except construction.
Lead containing material – inorganic lead plus lead soaps
Manufacturing
  Lead acid batteries
  Foundries
  Electronics
  Some Specialty Glass
  Organ Pipes
  Metal Recyclers
Maritime/shipbuilding and breaking
Firing Ranges
Facility maintenance exposures not covered by construction lead standard
Construction –
Defined as construction, alteration and/or repair, including painting and decorating:
  Demolition or salvage of structures where lead or materials containing lead are present
  Removal or encapsulation of materials containing lead
  New construction, alteration, repair, or renovation of structures, substrates, or portions thereof, that contain lead, or materials containing lead;
  Installation of products containing lead;
  Lead contamination/emergency cleanup;
  Transportation, disposal, storage, or containment of lead or materials containing lead on the site or location at which construction activities are performed; and
  Maintenance operations associated with the construction activities described in this section.

## Slide 4: Worker Rules for Lead Exposure
Requirements identical to OSHA
Exposure assessment exposure :
  Lead in the air (personal breathing zone monitoring)
    Action Level (AL) = 30 ug/m3
    Permissible Exposure Level (PEL) = 50 ug/m3 , 8 hour time-weighted-average (TWA8)
  Lead in dust on surfaces
    Surface Contamination remove to as “free as practical” level
  Blood lead levels (BLL) and Medical Surveillance
    Schedules vary for required Medical Surveillance Blood Lead Level (BLL) testing
      Medical removal at or over 40 ug/100g blood (construction)
      Medical removal at twice at/over 50ug/100g blood or single 60ug/100g blood (General industry)
4
Notes: Currently all state plans have requirements equivalent to OSHA – different numbering system in Washington.
Airborne exposure assessment use standard industrial hygiene protocols to measure lead in the air as a personal sample.
Surface swipe samples to access surface contamination and housekeeping “as free as practical”. Not tied to a number
ug/100 grams of blood equivalent to ug/dl
Medical surveillance requirements standards have different blood lead and medical exam schedules.
Medical removal levels reflect the differences between industries for timing and the change in adult background lead levels (early 80’s vs. 1993)

## Slide 5: The lead standards have many significant requirements mandated to protect workers from lead exposure including:
Hazard assessment and exposure evaluation with worker protection (PPE) during the assessment period
Exposure controls (like ventilation and work practices) to prevent worker exposure
Regulated areas to limit the number of exposed workers
Housekeeping – strict requirement for no loose lead dust
Worker decontamination, change areas to separate contaminated PPE from clean street clothes, eating areas, hand washing and showers, laundry
Worker Training
Medical monitoring and medical removal levels
Written program
5
Notes: DOSH General Industry & Construction Standards
Similarities
  Requires housekeeping practices
  Requires employer evaluation of worker airborne exposure
  Requires some level of blood lead evaluation (not identical)
  Requires exposure controls (e.g. exhaust ventilation)
Differences
  Exposure measures - construction is more task work specific (for presumed exposure levels aka “Trigger Tasks) General Industry has tasks in an appendix to the rule “known” to be over the PEL
  Showers – “where feasible” for construction (vs. required for general industry)
  Blood testing – for construction required for even 1 day of exposure (vs. prior to assignment if exposure greater than lead action level for 30 days)
  Employers are required to implement the standards to protect their employees.

## Slide 6: Industries with greatest number of cases – BLL > 25ug/dl, 2011-2014
Paint & Wall Covering Contractors - Bridge repair/painting workers
Firing range workers
Other Construction (includes steel demolition and erection)
Temporary Help Services
Boat Building and Ship Repair
Glass and Glass Product Manufacturing
Support Activities for Metal Mining
Other Industries…
6
Notes: Gun Ranges
DOSH only has jurisdiction over gun range operations when an employer-employee relationship exists
Little/no oversight of non-employer gun ranges
DOSH is in progress to inspect all suspected and known range operations in State again
Since March 2014, 21 inspections of 18 ranges has occurred
~ 35 employer-run ranges

## Slide 7: Rulemaking Discussions to Further Reduce Occupational Lead Exposure Activities
National Rulemaking
  Federal OSHA - no public action on lead rules at this time
  OSHA sets the minimum national standards on all rules
State Plan State activities
DOSH is monitoring discussions occurring in California
DOSH is hosting Lead Rules Stakeholder meetings: October 21,2015 at L&I Tukwila Office
Cal OSHA http://www.dir.ca.gov/dosh/DoshReg/5198Meetings.htm
Advisory group will meet for the sixth time in November 2015. Meetings started in 2011.
7
Notes: Cal OSHA and related
The 6th meeting will seek advice on the revised discussion drafts of section 1532.1 for Lead in Construction and section 5198 for Lead in General Industry. The revised discussion drafts and an agenda will be posted on this website and emailed to all interested parties prior to the meeting. Meetings started in 2011. 3 of the 6 public meetings have occurred in 2015.
Meeting schedule http://www.dir.ca.gov/dosh/DoshReg/5198Meetings.htm
Summary of general industry main “changes” http://www.dir.ca.gov/dosh/doshreg/5198-meetings/summary-of-draft-changes-03.25.15.pdf
Summary of construction main changes http://www.dir.ca.gov/dosh/DoshReg/Sum_of_Draft_Changes_03-25-15_for_4-21-15_AC.PDF
Flow diagram on general industry draft http://www.dir.ca.gov/dosh/doshreg/5198-meetings/lead-diagram-draft-1532.1.pdf
Flow diagram on construction draft http://www.dir.ca.gov/dosh/DoshReg/5198_Lead_Diagram_3-25-15.pdf
California Lead rules are essentially equivalent to Washington’s
Activities:
  California Department of Public Health made recommendations for a revised Permissible Exposure Limit (September 2013) and recommended changes to the standards
  California Department of Public Health held a webinar/seminar
  Cal-OSHA has had three public advisory meetings since 2013 to discuss proposals “Drafts under consideration”
Dept of Public Health https://www.cdph.ca.gov/Pages/DEFAULT.aspx
Recommendations https://www.cdph.ca.gov/programs/olppp/Pages/LeadStdRecs.aspx
Summary https://www.cdph.ca.gov/programs/olppp/Documents/LeadStdRev-At-A-Glance.pdf This has a next steps list at the end of the document

## Slide 8
Resources
Lead Topic Page http://www.lni.wa.gov/Safety/Topics/AtoZ/Lead/Default.asp
Complaints and Referrals
    http://www.lni.wa.gov/Safety/TrainingPrevention/Help/ReportHazards/complaints.asp
Consultation Requests
    http://www.lni.wa.gov/safety/Consultation/default.asp
  Rule making information
    http://www.lni.wa.gov/Safety/rules/?F=SHPN
8

## Slide 9: Questions
Technical questions on the Washington State Lead Standards
  Cheryl Christian, MS CIH
  360-902-5732
  Chrh235@lni.wa.gov